## Slide 1: RFC7999 BLACKHOLE BGP Community for Blackholing
Thomas King, DE-CIX
thomas.king@de-cix.net, @thking

## Slide 2: RFC7999 - BLACKHOLE BGP Community for Blackholing
To signal Blackholing different signaling mechanisms have been used:
Various BGP communities
Various pre-defined Next-Hop IP addresses
RFC7999 defines a well-known BLACKHOLE BGP Community (65535:666) that can be used at ISPs/IXPs
-> Signaling Blackholing could be everywhere the same

## Slide 3
If you offer a Blackholing service …
… please implement RFC7999
RFC7999 can be implemented in addition to existing signaling mechanisms

## Slide 4: ISPs/IXPs implementing RFC7999
ISPs:
  KPN, SysEleven, Strato, Individual Network Berlin e.V, Coloclue, Fusix Networks, BelWue
IXPs:
  MSK-IX, NETIX, NIX-CZ, TPIX.pl, SIX, France-IX, Equinix, LAIIX, Community-IX, CIX.HR, NYIIX, DE-CIX
You could be next on the list!
https://github.com/tking/BLACKHOLE-BGP-Community