## Slide 1: Are We There Yet? On RPKI Deployment and Security
Yossi Gilad
joint work with: Avichai Cohen,
Amir Herzberg, Michael Schapira, Haya Shulman

## Slide 2: The Resource Public Key Infrastructure
Intended to prevent prefix/subprefix hijacks
Lays the foundation for protection against more sophisticated attacks on interdomain routing
  BGPsec, SoBGP,…

## Slide 3: Prefix Hijacking
AS X
AS Y
AS 3320
AS 666
91.0.0.0/10
Path: 3320
91.0.0.0/10
Path: Y-3320
91.0.0.0/10
Path: 666
BGP Ad.
Data flow
prefers
shorter route

## Slide 4: Subprefix Hijacking
AS X
AS 3320
AS 666
91.0.0.0/10
Path: 3320
91.0.0.0/16
Path: Y-666
BGP Ad.
Data flow
Longest prefix match
Path length does not matter
AS Y
91.0.0.0/16
Path: 666

## Slide 5: Certifying Ownership with RPKI
RPKI assigns an IP prefix to a public key via a Resource Certificate (RC)
Owners can use their private key to issue a Route Origin Authorization (ROA)
ROAs identify ASes authorized to advertise an IP prefix in BGP

## Slide 6: Example: Certifying Ownership
Deutsche Telekom certified by RIPE for address space 91.0.0.0/10
91.0.0.0/10
Max-length = 10
AS 3320
RIPE
Réseaux IP Européens Network Coordination Centre
ROA
Legend:
Org with RC
Deutsche Telekom
91.0.0.0/10

## Slide 7: RPKI Can Prevent Prefix Hijacks
AS X
AS Y
AS 3320
AS 666
91.0.0.0/10
Path: Y-3320
91.0.0.0/10
Path: 666
BGP Ad.
Data flow
AS X uses the authenticated mapping (ROA) from 91.0/10 to
AS 3320 to discard the attacker’s route-advertisement
91.0.0.0/10
Max-length = 10
AS 3320

## Slide 8: Talk Outline
Challenges facing deployment
Route origin validation in partial deployment

## Slide 9: Insecure Deployment: Loose ROAs
AS 666
AS X
BGP Ad.
Data flow
AS A
1.2.0.0/16
Max-length = 16
AS A
ROA allows advertising only one /16 prefix
1.2.0.0/16
Path: A
Valid advertisement since AS A is the “origin”
1.2.0.0/16
Path: 666-A
Picks shorter path
Lychev et al. show that this attack is much less effective than prefix hijack

## Slide 10: Insecure Deployment: Loose ROAs
AS X
AS 666
BGP Ad.
Data flow
Longest-prefix-match
Path length does not matter
AS A
1.2.0.0/16
Max-length = 24
AS A
ROA allows advertising subprefixes up to length /24
AS A originates 1.2.0.0/16 but not 1.2.3.0/24
ROA is “loose”
1.2.0.0/16
Path: A
Valid advertisement since AS A is the “origin”
1.2.3.0/24
Path: 666-A
RFC 7115 mentions this attack

## Slide 11: Insecure Deployment: Loose ROAs
Loose ROAs are common!
  almost 30% of IP prefixes in ROAs
  89% of prefixes with maxLen > prefixLen
  manifests even in large providers!
Attacker can hijack all traffic to non-advertised subprefixes covered by a loose ROA
Vulnerability will be solved only when BGPsec is fully deployed, but a long way to go until then…
  better not to issue loose ROAs!

## Slide 12: Challenges to Deployment: Human Error
Many other mistakes in ROAs (see RPKI monitor)
  ``bad ROAs’’ cause legitimate prefixes to appear invalid
  filtering by ROAs may cause disconnection from legitimate destinations
  extensive measurements in [Iamartino et al., PAM’15]

## Slide 13: Improving Accuracy with ROAlert
roalert.org allows you to check whether your network is properly protected by ROAs
… and if not, why not

## Slide 14: Improving Accuracy with ROAlert
Online, proactive notification system
Retrieves ROAs from the RPKI and compares them against BGP advertisements
Alerts network operators about “loose ROAs” & “bad ROAs”

## Slide 15: Improving Accuracy with ROAlert
Initial results are promising!
  notifications reached 168 operators
  42% of errors were fixed within a month
ROAlert is:
  constantly monitoring (not only at registration)
  not opt-in
We advocate that ROAlert be adopted and adapted by RIRs!

## Slide 16: Talk Outline
Challenges facing deployment
Route origin validation in partial deployment

## Slide 17: Filtering Bogus Advertisements
Route-Origin Validation (ROV): use ROAs to discard/deprioritize route-advertisements from unauthorized origins [RFC 6811]
Verify:
signer authorized for subject prefix
signature is valid
BGP Routers
91.0.0.0/10:
AS = 3320, max-length = 10
RPKI pub. point
RCs and ROAs
Autonomous System
RPKI cache

## Slide 18: What is the Impact of Partial ROV Adoption?
Collateral benefit:
  Adopters protect ASes behind them by discarding invalid routes
Origin
AS 1
AS 2
AS 666
To: 1.1/16
AS path: 2-1
To: 1.1.1/24
AS path: 666
AS 3
AS 3 is only offered a good route
1.1.0.0/16
Max-length = 16
AS 1

## Slide 19: What is the Impact of Partial ROV Adoption?
Collateral damage: ASes not doing ROV might cause ASes that do ROV to fall victim to attacks!
  Disconnection: Adopters might be offered only bad routes
Origin
AS 1
AS 2
AS 666
To: 1.1/16
AS path: 1
To: 1.1/16
AS path: 2-666
AS 3
AS 2 prefers to advertise routes from AS 666 over AS 1
AS 3 receives only bad advertisement and disconnects from 1.1/16
1.1.0.0/16
Max-length = 16
AS 1

## Slide 20: What is the Impact of Partial ROV Adoption?
Collateral damage: ASes not doing ROV might cause ASes that do ROV to fall victim to attacks!
  Control-Plane-Data-Plane Mismatch! data flows to attacker, although AS 3 discarded it
Origin
AS 1
AS 2
AS 666
AS 3
To: 1.1/16
AS path: 2-1
To: 1.1.1/24
AS path: 2-666
AS 2 advertises both prefix & subprefix routes
AS 3 discards bad subprefix route
AS 2 does not filter and uses bad route for subprefix
1.1.0.0/16
Max-length = 16
AS 1

## Slide 21: Quantify Security in Partial Adoption: Simulation Framework
B
D
H
J
E
I
G
K
L
F
1.1.0.0/16
Max-length = 16
AS A
C
A
Pick victim & attacker
Victim’s prefix has a ROA
Pick set of ASes doing ROV
Evaluate which ASes send traffic to the attacker
  Empirically-derived AS-level network from CAIDA
    Including inferred peering links [Giotsas et al., SIGCOMM’13]

## Slide 22: Quantify Security in Partial Adoption
Top ISP adopts with probability p
Significant benefit only when p is high
Prefix hijack success rate
Subprefix hijack success rate

## Slide 23: Conclusion: What Can We Improve?
Information accuracy
  ROAlert informs & alerts operators about:
    Bad ROAs
    Loose ROAs
Preventing hijacks
  Incentivize ROV adoption by the top ISPs!

## Slide 24: Thank You!
This work appeared at NDSS’17
Tech report at https://eprint.iacr.org/2016/1010.pdf
Questions? 